## Slide 1: Approaching Zero Driver Overhead
Cass Everitt NVIDIA
Tim Foley Intel
Graham Sellers AMD
John McDonald NVIDIA

## Slide 2: Cass Everitt
NVIDIA

## Slide 3: Assertion
OpenGL already has paths with very low driver overhead
You just need to know
  What they are, and
  How to use them

## Slide 4: But first, who are we?
Graham Sellers @GrahamSellers
  AMD OpenGL driver manager, OpenGL SuperBible author
Tim Foley @TangentVector
  Graphics researcher, GPU language/compiler nerd
John McDonald @basisspace
  Graphics engineer, chip architect, game developer
Cass Everitt @casseveritt
  GL zealot, chip architect, mobile enthusiast

## Slide 5: Many kinds of bottlenecks
Focus here is “driver limited”
  App could render more, and
  GPU could render more, but
  Driver is at its limit…
    Because of expensive API calls

## Slide 6: Some causes of driver overhead
The CPU cost of fulfilling the API contract
Validation
Hazard avoidance

## Slide 7: Costs that add up…
Major Categories:
  synchronization, allocation, validation, and compilation
Buffer updates (synchronization, allocation)
  Mapping, in-band updates
Binding objects (validation, compilation)
  FBOs, programs, textures, buffers

## Slide 8: Remedy? – Efficient APIs!
Buffer storage
Texture arrays
Multi-Draw Indirect
  Texture arrays, bindless, sparse, indirect parameters
}
Tim Foley
Graham Sellers
}

## Slide 9: Results
apitest
  Framework for testing different “solutions”
  Source on github
}
John McDonald

## Slide 10: Remember, these OpenGL APIs
Exist TODAY – already on your PC
Are at least multi-vendor (EXT), and mostly core (GL 4.2+)
Coexist with existing OpenGL

## Slide 11: Remember, these OpenGL APIs
Exist TODAY – already on your PC
Are at least multi-vendor (EXT), and mostly core (GL 4.2+)
Coexist with existing OpenGL

## Slide 12: Remember, these OpenGL APIs
Exist TODAY – already on your PC
Are at least multi-vendor (EXT), and mostly core (GL 4.2+)
Coexist with existing OpenGL

## Slide 13: On with the show…
next
speaker

## Slide 14: Tim Foley
Intel

## Slide 15: Challenge: More Stuff per Frame
Varied
  Not 1000s of same instanced mesh
  Unique geometry, textures, etc.
Dynamic
  Not just pretty skinned meshes
  Generate new geometry each frame

## Slide 16: Want an Order of Magnitude
Increase in unique objects per frame
  Can over-simplify as draws per frame, but
  Misses importance of variety
Do we need a new API to achieve this?
  How far can we get with what we have today?

## Slide 17: Three Techniques in This Talk
Persistent-mapped buffers
  Faster streaming of dynamic geometry
MultiDrawIndirect (MDI)
  Faster submission of many draw calls
Packing 2D textures into arrays
  Texture changes no longer break batches

## Slide 18: Naïve Draw Loop
foreach( object )
{
// bind framebuffer
// set depth, blending, etc. states
// bind shaders
// bind textures
// bind vertex/index buffers
WriteUniformData( object );
glDrawElements(
GL_TRIANGLES,
object->indexCount,
GL_UNSIGNED_SHORT,
0 );
}

## Slide 19: Typical Draw Loop
// sort or bucket visible objects
foreach( render target ) // framebuffer
foreach( pass ) // depth, blending, etc. states
foreach( material ) // shaders
foreach( material instance ) // textures
foreach( vertex format ) // vertex buffers
foreach( object )
{
WriteUniformData( object );
glDrawElementsBaseVertex(
GL_TRIANGLES,
object->indexCount,
GL_UNSIGNED_SHORT,
object->indexDataOffset,
object->baseVertex );
}

## Slide 20: Two Ways to Improve Overhead
// sort or bucket visible objects
foreach( render target ) // framebuffer
foreach( pass ) // depth, blending, etc. states
foreach( material ) // shaders
foreach( material instance ) // textures
foreach( vertex format ) // vertex buffers
foreach( object )
{
WriteUniformData( object );
glDrawElementsBaseVertex(
GL_TRIANGLES,
object->indexCount,
GL_UNSIGNED_SHORT,
object->indexDataOffset,
object->baseVertex );
}
submit each batch faster
fewer, bigger batches

## Slide 21: Pack Multiple Objects per Buffer
// sort or bucket visible objects
foreach( render target ) // framebuffer
foreach( pass ) // depth, blending, etc. states
foreach( material ) // shaders
foreach( material instance ) // textures
foreach( vertex format ) // vertex buffers
foreach( object )
{
WriteUniformData( object );
glDrawElementsBaseVertex(
GL_TRIANGLES,
object->indexCount,
GL_UNSIGNED_SHORT,
object->indexDataOffset,
object->baseVertex );
}
pack multiple objects into the same
(dynamic or static) vertex/index buffer
take advantage of glDraw*() params to
index into buffer without changing bindings

## Slide 22: Dynamic Streaming of Geometry
Typical dynamic vertex ring buffer
void* data = glMapBuffer(GL_ARRAY_BUFFER,
ringOffset,
dataSize,
GL_MAP_UNSYNCHRONIZED_BIT
| GL_MAP_WRITE_BIT );
WriteGeometry( data, ... );
glUnmapBuffer(GL_ARRAY_BUFFER);
ringOffset += dataSize;
// deal with wrap-around in ring, etc.
frequent mapping = overhead
no sync with GPU, but forces
sync in multi-threaded drivers

## Slide 23: BufferStorage and Persistent Map
Allocate buffer with glBufferStorage()
Use flags to enable persistent mapping
glBufferStorage(GL_ARRAY_BUFFER, ringSize, NULL, flags);
GLbitfield flags = GL_MAP_WRITE_BIT
| GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
keep mapped while drawing
writes automatically visible to GPU

## Slide 24: Dynamic Streaming of Geometry
Map once at creation time
No more Map/Unmap in your draw loop
  But need to do synchronization yourself
data = glMapBufferRange(ARRAY_BUFFER, 0, ringSize, flags);
WriteGeometry( data, ... );
data += dataSize;
upcoming talks will cover
glFenceSync() and glClientWaitSync()

## Slide 25: Performance
BufferSubData vs Map(UNSYNCHRONIZED)
  Intel: avoid frequent BufferSubData()
  NV: Map(UNSYNCH) bad for threaded drivers
Persistent mapping best where supported
  Overhead 2-20x better than next best option

## Slide 26: That Inner Loop Again
foreach( object )
{
WriteUniformData( object, &uniformData );
glDrawElementsBaseVertex(
GL_TRIANGLES,
object->indexCount,
GL_UNSIGNED_SHORT,
object->indexDataOffset,
object->baseVertex );
}

## Slide 27: Using an Indirect Draw
DrawElementsIndirectCommand command;
foreach( object )
{
WriteUniformData( object, &uniformData );
WriteDrawCommand( object, &command );
glDrawElementsIndirect(
GL_TRIANGLES,
GL_UNSIGNED_SHORT,
&command );
}
typedef struct {
uint count;
uint instanceCount;
uint firstIndex;
uint baseVertex;
uint baseInstance; } DrawElementsIndirectCommand;
per-object parameters are
now sourced from memory

## Slide 28: One Multi-Draw Submits it All
DrawElementsIndirectCommand* commands = ...;
foreach( object )
{
WriteUniformData( object, &uniformData[i] );
WriteDrawCommand( object, &commands[i] );
}
glMultiDrawElementsIndirect(
GL_TRIANGLES,
GL_UNSIGNED_SHORT,
commands,
commandCount,
0 );
fill in per-object data
(use parallelism, GPU compute if you like)
kick buffered-up objects to be rendered

## Slide 29: What if I don’t know the count?
Doing GPU culling, etc.
Use ARB_indirect_parameters
  Caveat: not all HW/drivers support it
glBindBuffer( GL_DRAW_INDIRECT_BUFFER, commandBuffer );
glBindBuffer( GL_PARAMETER_BUFFER, countBuffer );
// …
glMultiDrawElementsIndirectCount(
GL_TRIANGLES, GL_UNSIGNED_SHORT,
commandOffset,
countOffset,
maxCommandCount,
0 );

## Slide 30: Per-Draw Parameters/Data
If shader used to take struct of uniforms
Now take an array of such structs
Or use SSBO to go bigger
uniform ShaderParams params;
(Shader Storage Buffer Object)
uniform ShaderParams params[MAX_BATCH_SIZE];
buffer AllTheParams { ShaderParams params[]; };

## Slide 31: How to find your draw’s data?
Ideally, just index it using gl_DrawID
  Provided by ARB_shader_draw_parameters
Not supported everywhere
  But relatively simple to implement your own
mat4 mvp = params[gl_DrawIDARB].mvp;

## Slide 32: Implement Your Own Draw ID
Use baseInstance field of draw struct
  Increment base instance for each command
Shader can’t see base instance
  gl_InstanceID always counts from zero
http://www.g-truc.net/post-0518.html
cmd->baseInstance = drawCounter++;

## Slide 33: Implement Your Own Draw ID
Use a vertex attribute
  Set as per-instance with glVertexAttribDivisor
Fill buffer with your own IDs
  Or arbitrary other per-draw parameters
On some HW, faster than using gl_DrawID

## Slide 34: More MultiDrawIndirect Caveats
If generating draws on GPU
  Use a GL buffer (obviously)
If generating on CPU
  Intel: (Compat) faster to use ordinary host pointer
  NV: persistent-mapped buffer slightly faster
GPU or CPU
  AMD: Array must be tightly packed for best perf
Notes: Where tightly packed == sizeof(struct) with no additional data

## Slide 35: Can Be 6-10x Less Overhead
Chart: Normalized Objects per Second
| Dynamic Buffer | Persistent-Mapped | Multi-Draw
Series 1 | 1 | 3.7692 | 6.1211

## Slide 36: Batching Across Texture Changes
Bindless, sparse can help
  As you will hear
Not all hardware supports these
Packing 2D textures into arrays
  Works on all current hardware/drivers

## Slide 37: Packing Textures Into Arrays
Array groups textures with same shape
  Dimensions, format, mips, MSAA
Texture views may allow further grouping
  Put some same-size formats together

## Slide 38: Packing Textures Into Arrays
Bind all arrays to pipeline at once
Need to allocate carefully
  Based on your content requirements
  Don’t allocate more than fits in GPU memory
uniform sampler2Darray allSamplers[MAX_ARRAY_TEXTURES];

## Slide 39: Options for Sampler Parameters
Pair array with different sampler objs
Create views of array with different state
Be careful about max texture limits
  Each combination needs a new binding slot

## Slide 40: Accessing Packed 2D Textures
Texture “handle” is pair of indices
  Index into array of sampler2Darray
  Slice index into particular array texture
Can store as 64 bits {int;float;}
Or pack into 32 bits (hi/lo)
no int→float convert in shader
fewer bytes to read, but more math

## Slide 41: Texture Array ~5x Less Overhead
Chart: Normalized Objects per Second
| glBindTexture per Object | Texture Arrays | No Texture
Series 1 | 1 | 4.8198 | 4.9675

## Slide 42: Dramatically Reduced Overhead
Possible with current GL API and HW
Persistent-mapped buffers
Indirect and Multi-Draws
Packing 2D textures into arrays
Overhead is priority for all of us on GL

## Slide 43: Graham Sellers
AMD

## Slide 44: Section Overview
Bindless textures
  Recap of traditional texture binding
  Remove texture units with bindless
Sparse textures
  Manage virtual and physical memory
  Streaming, sparse data sets, etc.

## Slide 45: Texture Units - Recap
Traditional texture binding
  Create textures
  Bind to texture units
  Declare samplers in shaders
  Draw

## Slide 46: Texture Units - Recap
Textures bound to numbered units
  Limited number of texture units
  State changes between draws
  Driver controls residency

## Slide 47: Texture Units - Recap
Binding textures - API
Very hard to coalesce draws
glGenTextures(10, &tex[0]);
glBindTexture(GL_TEXTURE_2D, tex[n]);
glTexStorage2D(GL_TEXTURE_2D, ...);
foreach (draw in draws) {
foreach (texture in draw->textures) {
glBindTexture(GL_TEXTURE_2D, tex[texture]);
}
// Other stuff
glDrawElements(...);
}

## Slide 48: Texture Units - Recap
Binding textures - shader
Limited textures per shader
  All declared at global scope
layout (binding = 0) uniform sampler2D uTexture1;
layout (binding = 1) uniform sampler3D uTexture2;
out vec4 oColor;
void main(void){
oColor = texture(uTexture1, ...) +
texture(uTexture2, ...);
}

## Slide 49: Bindless Textures
Remove texture bindings!
  Unlimited* virtual texture bindings
  Application controls residency
  Shader accesses textures by handle
* Virtually unlimited

## Slide 50: Bindless Textures
Bindless textures - API
No texture binds between draws
// Create textures as normal, get handles from textures
GLuint64 handle = glGetTextureHandleARB(tex);
// Make resident
glMakeTextureHandleResidentARB(handle);
// Communicate ‘handle’ to shader... somehow
foreach (draw) {
glDrawElements(...);
}

## Slide 51: Bindless Textures
Bindless textures - shader
Shader accesses textures by handle
  Must communicate handles to shader
uniform Samplers {
sampler2D tex[500]; // Limited only by storage
};
out vec4 oColor;
void main(void) {
oColor = texture(tex[123], ...) + texture(tex[456], ...);
}

## Slide 52: Bindless Textures
Handles are 64-bit integers
  Stick them in uniform buffers
    Switch set of textures – glBindBufferRange
    Number of accessible textures limited by buffer size
  Put them in structures (AoS)
    Index with gl_DrawIDARB, gl_InstanceID

## Slide 53: Bindless Textures – DANGER!!!
Some caveats with bindless textures
  Divergence rules apply
    Just like indexing arrays of textures
    Bindless handle must be constant across instance
  Divergence might work
    On some implementations, it Just Works
    On others, it Just Doesn’t
    Even when it works, it could be expensive

## Slide 54: Sparse Textures
Very large virtual textures
  Separate virtual and physical allocation
  Partially populated arrays, mips, cubes, etc.
  Stream data on demand

## Slide 55: Sparse Textures
Textures arranged as tiles
  Each tile may be resident or not

## Slide 56: Sparse Textures
Sparse textures – API
That’s it – now you have a virtual texture
// Tell OpenGL you want a sparse texture
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_SPARSE_ARB, GL_TRUE);
// Allocate storage
glTexStorage2D(GL_TEXTURE_2D, 10, GL_RGBA8, 1024, 1024);

## Slide 57: Sparse Textures
Sparse textures – page sizes
// Query number of available page sizes
glGetInternalformativ(GL_TEXTURE_2D, GL_NUM_VIRTUAL_PAGE_SIZES_ARB,
GL_RGBA8, sizeof(GLint), &num_sizes);
// Get actual page sizes
glGetInternalformativ(GL_TEXTURE_2D, GL_VIRTUAL_PAGE_SIZE_X_ARB,
GL_RGBA8, sizeof(page_sizes_x),
&page_sizes_x[0]);
glGetInternalformativ(GL_TEXTURE_2D, GL_VIRTUAL_PAGE_SIZE_Y_ARB,
GL_RGBA8, sizeof(page_sizes_y),
&page_sizes_y[0]);
// Choose a page size
glTexParameteri(GL_TEXTURE_2D, GL_VIRTUAL_PAGE_SIZE_INDEX_ARB, n);

## Slide 58: Sparse Textures
Reserve and commit
  In ‘Operating System’ terms
    Reserve – virtual allocation without physical store
    Commit – back virtual allocation with real memory

## Slide 59: Sparse Textures
Sparse textures – commitment
  Commitment is controlled by a single function
  Uncommitted pages use no memory
  Committed pages may contain data
void glTexPageCommitmentARB(GLenum target, GLint level,
GLint xoffset, GLint yoffset,
GLint zoffset, GLsizei width,
GLsizei height, GLsizei depth,
GLboolean commit);

## Slide 60: Sparse Textures
Sparse textures – data storage
  Put data into sparse textures as normal
    glTexSubImage, glCopyTextureImage, etc.
      Use a (persistent mapped) PBO for this!
    Attach to framebuffer object + draw
  Read from sparse textures
    glReadPixels, glGetTexImage*, etc.

## Slide 61: Sparse Textures
Sparse textures – in-shader use
  No changes to shaders
    Reads from committed regions behave normally
    Reads from uncommitted regions return junk
      Probably not junk – most likely zeros
      The spec doesn’t mandate this, however

## Slide 62: Sparse Texture Arrays
Combine sparse textures and arrays
  Create very long (sparse) array textures
  Some layers are resident, some are not
  Allocate new layers on demand
    New layer = glTexPageCommitmentARB

## Slide 63: Sparse Texture Arrays
Manage your own texture memory
  Create a huge virtual array texture
  Need a new texture?
    Allocate a new layer
  Don’t need it any more?
    Recycle or make non-resident

## Slide 64: Sparse Bindless Texture Arrays
Use all the features!
  Create a sparse array per texture size
  As textures become needed, commit pages
    Run out of pages? Make another texture...
  Get texture bindless handles
  Use as many handles as you like

## Slide 65: Sparse Bindless Texture Arrays
Indexing sparse bindless arrays requires:
  64-bit texture handle
  N-bit layer index
Remember...
  Index can diverge, handle cannot
Need one array per-size

## Slide 66: Building Data Structures
Okay, so how do we use these things?
  Option 1 – Build on the CPU
    It’s just memory writes
    Use a bunch of threads
    Persistent maps
  Option 2 – Use the GPU
    Much fun. Wow.

## Slide 67: Building Data Structures
Using the GPU to set the scene (1)
  Create SSBO with AoS for draw parameters
struct DrawParams {
uint count;
uint instanceCount;
uint firstIndex;
uint baseIndex;
uint baseInstance;
};
layout (binding = 0) {
DrawParams draw_params[];
};

## Slide 68: Building Data Structures
Using the GPU to set the scene (2)
  Create another SSBO for draw metadata
struct DrawMeta {
uint material_index;
// More per-draw meta-stuff goes here...
};
layout (binding = 0) {
DrawMeta draw_meta[];
};

## Slide 69: Building Data Structures
Using the GPU to set the scene (3)
  Use atomic counter to append to buffers
layout (binding = 0, offset = 0) atomic_uint draw_count;
void append_draw(DrawParams params, DrawMeta meta)
{
uint index = atomicCounterIncrement(draw_count);
draw_params[index] = params;
draw_meta[index] = meta;
}

## Slide 70: Building Data Structures
Using the GPU to set the scene (4)
  Dump counter, do MultiDraw*IndirectCount
glCopyBufferSubData(GL_ATOMIC_COUNTER_BUFFER,
GL_PARAMETER_BUFFER_ARB,
0, 0, sizeof(GLuint));
glMultiDrawElementsIndirectCountARB(GL_TRIANLGES,
GL_UNSIGNED_SHORT,
nullptr,
MAX_DRAWS,
0);

## Slide 71: Building Data Structures
Using the GPU to set the scene (5)
  In draw, use meta with gl_DrawIDARB
struct Material {
sampler2D tex1; };
layout (binding = 0) uniform MaterialData {
Material material[]; };
...
oColor = texture(material[draw_meta[gl_DrawIDARB].material_index],
...);

## Slide 72: John McDonald
NVIDIA

## Slide 73: Putting it all into practice
Introducing apitest
Results
Code review

## Slide 74: apitest
https://github.com/nvMcJohn/apitest
Extensible OSS Framework (Public Domain)
Uses SDL 2.0 (Thanks SDL!)
Initially developed by Patrick Doane
OS | OpenGL | D3D11
Windows | Yes | Yes
Linux | Yes | No
OSX | Sorta | No
Notes: * OSX is supported, but it currently really only runs the NULL solution.

## Slide 75: The Framework
Code is segmented into Problems and Solutions
A Problem is a dataset to render
A Solution is one targeted approach to rendering that dataset (Problem)
Support code to create shaders, load textures, etc.

## Slide 76: The Problems So Far
DynamicStreaming
  Render 160,000 “particles” that are dynamically generated each frame
UntexturedObjects
  Render 643 different, untextured objects
  Different matrices per object
  No instancing allowed!
Notes: 64^3 = 262,144

## Slide 77: The Problems So Far - Continued
Textured Quads
  10,000 quads using different textures
  Texture is changed between every object
Null
  Clear and SwapBuffer
  Not going to discuss today—included as a sanity startup.

## Slide 78: Result discussion
Results gathered on a GTX 680, using public driver 335.23.
But are shown normalized.
AMD and Intel have very similar performance ratios between solutions.

## Slide 79: Decoder Ring
SBTA = Sparse Bindless Texture Array
SDP = Shader Draw Parameters

## Slide 80: DynamicStreaming
Demo!
Problem: Render 160,000 “particles” that are dynamically generated each frame

## Slide 82
Chart: DynamicStreaming - Normalized Obj/s
| GLMapPersistent | D3D11MapNoOverwrite | GLBufferSubData | D3D11UpdateSubresource | GLMapUnsynchronized
Normalized fps | 2.0445 | 1 | 0.50171 | 0.066583 | 0.042863

## Slide 83: GLMapPersistent
Map the buffer at the beginning of time
Keep it mapped forever.
You are responsible for safety (proper fencing)
Do not stomp on data in flight
src/solutions/dynamicstreaming/gl/mappersistent.*

## Slide 84: Required Extensions
ARB_buffer_storage
ARB_map_buffer_range
ARB_sync

## Slide 85: Buffer Creation
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_MAP_DYNAMIC_STORAGE_BIT;
mDestHead = 0;
mBuffSize = 3 * maxVerts * kVertexSizeBytes;
glBindBuffer(GL_ARRAY_BUFFER, mVertexBuffer);
glBufferStorage(GL_ARRAY_BUFFER, mBuffSize, nullptr, createFlags);
mVertexDataPtr = glMapBufferRange(GL_ARRAY_BUFFER, 0, mBuffSize, mapFlags);
Notes: mVertexBuffer was previously gen’d into with glGenBuffers(1, &mVertexBuffer);
We set up for triple buffering. You can often get away with a smaller buffer (like 2x). You need to measure.
Our flags are the WRITE, PERSISTENT and COHERENT bits.
Then we persistently map the whole buffer.

## Slide 86: Dem Flags
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_MAP_DYNAMIC_STORAGE_BIT;
mDestHead = 0;
mBuffSize = 3 * maxVerts * kVertexSizeBytes;
glBindBuffer(GL_ARRAY_BUFFER, mVertexBuffer);
glBufferStorage(GL_ARRAY_BUFFER, mBuffSize, nullptr, createFlags);
mVertexDataPtr = glMapBufferRange(GL_ARRAY_BUFFER, 0, mBuffSize, mapFlags);
Notes: mVertexBuffer was previously gen’d into with glGenBuffers(1, &mVertexBuffer);
We set up for triple buffering. You can often get away with a smaller buffer (like 2x). You need to measure.
Our flags are the WRITE, PERSISTENT and COHERENT bits.
Then we persistently map the whole buffer.

## Slide 87: Set circular buffer head
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_MAP_DYNAMIC_STORAGE_BIT;
mDestHead = 0;
mBuffSize = 3 * maxVerts * kVertexSizeBytes;
glBindBuffer(GL_ARRAY_BUFFER, mVertexBuffer);
glBufferStorage(GL_ARRAY_BUFFER, mBuffSize, nullptr, createFlags);
mVertexDataPtr = glMapBufferRange(GL_ARRAY_BUFFER, 0, mBuffSize, mapFlags);
Notes: mVertexBuffer was previously gen’d into with glGenBuffers(1, &mVertexBuffer);
We set up for triple buffering. You can often get away with a smaller buffer (like 2x). You need to measure.
Our flags are the WRITE, PERSISTENT and COHERENT bits.
Then we persistently map the whole buffer.

## Slide 88: Triple Buffering ftw
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_MAP_DYNAMIC_STORAGE_BIT;
mDestHead = 0;
mBuffSize = 3 * maxVerts * kVertexSizeBytes;
glBindBuffer(GL_ARRAY_BUFFER, mVertexBuffer);
glBufferStorage(GL_ARRAY_BUFFER, mBuffSize, nullptr, createFlags);
mVertexDataPtr = glMapBufferRange(GL_ARRAY_BUFFER, 0, mBuffSize, mapFlags);
Notes: mVertexBuffer was previously gen’d into with glGenBuffers(1, &mVertexBuffer);
We set up for triple buffering. You can often get away with a smaller buffer (like 2x). You need to measure.
Our flags are the WRITE, PERSISTENT and COHERENT bits.
Then we persistently map the whole buffer.

## Slide 89: Buffer Create
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_MAP_DYNAMIC_STORAGE_BIT;
mDestHead = 0;
mBuffSize = 3 * maxVerts * kVertexSizeBytes;
glBindBuffer(GL_ARRAY_BUFFER, mVertexBuffer);
glBufferStorage(GL_ARRAY_BUFFER, mBuffSize, nullptr, createFlags);
mVertexDataPtr = glMapBufferRange(GL_ARRAY_BUFFER, 0, mBuffSize, mapFlags);
Notes: mVertexBuffer was previously gen’d into with glGenBuffers(1, &mVertexBuffer);
We set up for triple buffering. You can often get away with a smaller buffer (like 2x). You need to measure.
Our flags are the WRITE, PERSISTENT and COHERENT bits.
Then we persistently map the whole buffer.

## Slide 90: Map me… forever.
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT
| GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_MAP_DYNAMIC_STORAGE_BIT;
mDestHead = 0;
mBuffSize = 3 * maxVerts * kVertexSizeBytes;
glBindBuffer(GL_ARRAY_BUFFER, mVertexBuffer);
glBufferStorage(GL_ARRAY_BUFFER, mBuffSize, nullptr, createFlags);
mVertexDataPtr = glMapBufferRange(GL_ARRAY_BUFFER, 0, mBuffSize, mapFlags);
Notes: mVertexBuffer was previously gen’d into with glGenBuffers(1, &mVertexBuffer);
We set up for triple buffering. You can often get away with a smaller buffer (like 2x). You need to measure.
Our flags are the WRITE, PERSISTENT and COHERENT bits.
Then we persistently map the whole buffer.

## Slide 91: Buffer Update / Render
mBufferLockManager.WaitForLockedRange(mDstHead, vertSizeBytes);
for (int i = 0; i < particleCount; ++i) {
const int vertexOffset = i * kVertsPerParticle;
const int thisDstOffset = mDstHead + (i * kParticleSizeBytes);
void* dst = (unsigned char*) mVertexDataPtr + thisDstOffset;
memcpy(dst, &_vertices[vertexOffset], kParticleSizeBytes);
DrawArrays(TRIANGLES, kStartIndex + vertexOffset, kVertsPerParticle);
}
mBufferLockManager.LockRange(mDstHead, vertSizeBytes);
mDstHead = (mDstHead + vertSizeBytes) % mBuffSize;

## Slide 92: Safety Third!
mBufferLockManager.WaitForLockedRange(mDstHead, vertSizeBytes);
for (int i = 0; i < particleCount; ++i) {
const int vertexOffset = i * kVertsPerParticle;
const int thisDstOffset = mDstHead + (i * kParticleSizeBytes);
void* dst = (unsigned char*) mVertexDataPtr + thisDstOffset;
memcpy(dst, &_vertices[vertexOffset], kParticleSizeBytes);
DrawArrays(TRIANGLES, kStartIndex + vertexOffset, kVertsPerParticle);
}
mBufferLockManager.LockRange(mDstHead, vertSizeBytes);
mDstHead = (mDstHead + vertSizeBytes) % mBuffSize;

## Slide 93: Write those particles
mBufferLockManager.WaitForLockedRange(mDstHead, vertSizeBytes);
for (int i = 0; i < particleCount; ++i) {
const int vertexOffset = i * kVertsPerParticle;
const int thisDstOffset = mDstHead + (i * kParticleSizeBytes);
void* dst = (unsigned char*) mVertexDataPtr + thisDstOffset;
memcpy(dst, &_vertices[vertexOffset], kParticleSizeBytes);
DrawArrays(TRIANGLES, kStartIndex + vertexOffset, kVertsPerParticle);
}
mBufferLockManager.LockRange(mDstHead, vertSizeBytes);
mDstHead = (mDstHead + vertSizeBytes) % mBuffSize;

## Slide 94: Now draw (inefficiently)
mBufferLockManager.WaitForLockedRange(mDstHead, vertSizeBytes);
for (int i = 0; i < particleCount; ++i) {
const int vertexOffset = i * kVertsPerParticle;
const int thisDstOffset = mDstHead + (i * kParticleSizeBytes);
void* dst = (unsigned char*) mVertexDataPtr + thisDstOffset;
memcpy(dst, &_vertices[vertexOffset], kParticleSizeBytes);
DrawArrays(TRIANGLES, kStartIndex + vertexOffset, kVertsPerParticle);
}
mBufferLockManager.LockRange(mDstHead, vertSizeBytes);
mDstHead = (mDstHead + vertSizeBytes) % mBuffSize;

## Slide 95: Update circular buffer head
mBufferLockManager.WaitForLockedRange(mDstHead, vertSizeBytes);
for (int i = 0; i < particleCount; ++i) {
const int vertexOffset = i * kVertsPerParticle;
const int thisDstOffset = mDstHead + (i * kParticleSizeBytes);
void* dst = (unsigned char*) mVertexDataPtr + thisDstOffset;
memcpy(dst, &_vertices[vertexOffset], kParticleSizeBytes);
DrawArrays(TRIANGLES, kStartIndex + vertexOffset, kVertsPerParticle);
}
mBufferLockManager.LockRange(mDstHead, vertSizeBytes);
mDstHead = (mDstHead + vertSizeBytes) % mBuffSize;

## Slide 96: UntexturedObjects
Demo!
Problem: Render 643 unique, untextured objects

## Slide 98
Chart: Untextured Object - Normalized Obj/s
| GLBufferStorage-NoSDP | GLMultiDrawBuffer-NoSDP | GLMultiDraw-NoSDP | GLBufferStorage-SDP | GLMultiDrawBuffer-SDP | GLMultiDraw-SDP | GLMapPersistent | GLDrawLoop | GLBindlessIndirect | GLTexCoord | GLUniform | D3D11Naive | GLBindless | GLDynamicBuffer | GLBufferRange | GLMapUnsynchronized
 | 8.1115 | 7.0616 | 5.833 | 4.633 | 3.6499 | 3.333 | 2.0921 | 1.9154 | 1.588 | 1.1828 | 1.1449 | 1 | 0.86654 | 0.65044 | 0.59761 | 0.034548

## Slide 99
Chart: Untextured Object - Normalized Obj/s
| GLBufferStorage-NoSDP | GLMultiDrawBuffer-NoSDP | GLMultiDraw-NoSDP | GLBufferStorage-SDP | GLMultiDrawBuffer-SDP | GLMultiDraw-SDP | GLMapPersistent | GLDrawLoop | GLBindlessIndirect | GLTexCoord | GLUniform | D3D11Naive | GLBindless | GLDynamicBuffer | GLBufferRange | GLMapUnsynchronized
 | 8.1115 | 7.0616 | 5.833 | 4.633 | 3.6499 | 3.333 | 2.0921 | 1.9154 | 1.588 | 1.1828 | 1.1449 | 1 | 0.86654 | 0.65044 | 0.59761 | 0.034548

## Slide 100
Chart: Untextured Object - Normalized Obj/s
| GLBufferStorage-NoSDP | GLMultiDrawBuffer-NoSDP | GLMultiDraw-NoSDP | GLBufferStorage-SDP | GLMultiDrawBuffer-SDP | GLMultiDraw-SDP | GLMapPersistent | GLDrawLoop | GLBindlessIndirect | GLTexCoord | GLUniform | D3D11Naive | GLBindless | GLDynamicBuffer | GLBufferRange | GLMapUnsynchronized
 | 8.1115 | 7.0616 | 5.833 | 4.633 | 3.6499 | 3.333 | 2.0921 | 1.9154 | 1.588 | 1.1828 | 1.1449 | 1 | 0.86654 | 0.65044 | 0.59761 | 0.034548

## Slide 101
Chart: Untextured Object - Normalized Obj/s
| GLBufferStorage-NoSDP | GLMultiDrawBuffer-NoSDP | GLMultiDraw-NoSDP | GLBufferStorage-SDP | GLMultiDrawBuffer-SDP | GLMultiDraw-SDP | GLMapPersistent | GLDrawLoop | GLBindlessIndirect | GLTexCoord | GLUniform | D3D11Naive | GLBindless | GLDynamicBuffer | GLBufferRange | GLMapUnsynchronized
 | 8.1115 | 7.0616 | 5.833 | 4.633 | 3.6499 | 3.333 | 2.0921 | 1.9154 | 1.588 | 1.1828 | 1.1449 | 1 | 0.86654 | 0.65044 | 0.59761 | 0.034548

## Slide 102: GLBufferStorage-(ε|No)SDP
Set up a giant uniform or storage buffer with data for all objects for a frame.
Use MDI to render many objects at once
And PMB for dynamic data (matrix transforms, MDI entries)
Need a way to index data in shader (SDP)

## Slide 103: Required Extensions
ARB_buffer_storage
ARB_map_buffer_range
ARB_multi_draw_indirect
ARB_shader_draw_parameters
ARB_shader_storage_buffer_object
ARB_sync

## Slide 104: NoSDP
Can be used when instancing isn’t needed
Very simple improvement to SDP approach
Not going to cover today
  So check the source code!

## Slide 105: DrawElementsIndirectCommand
struct DrawElementsIndirectCommand
{
uint count;
uint instanceCount;
uint firstIndex;
uint baseVertex;
uint baseInstance;
};
typedef DrawElementsIndirectCommand DEICmd;

## Slide 106: Cmd Buffer Creation
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT | GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_DYNAMIC_STORAGE_BIT;
mCmdHead = 0;
mCmdSize = 3 * objCount * sizeof(DEICmd);
glBindBuffer(GL_DRAW_INDIRECT_BUFFER, mCmdBuffer);
glBufferStorage(GL_DRAW_INDIRECT_BUFFER, mCmdSize, 0, createFlags);
mCmdPtr = glMapBufferRange(GL_DRAW_INDIRECT_BUFFER, 0, mCmdSize, mapFlags);

## Slide 107: Obj Buffer Creation
GLbitfield mapFlags = GL_MAP_WRITE_BIT | GL_MAP_PERSISTENT_BIT | GL_MAP_COHERENT_BIT;
GLbitfield createFlags = mapFlags | GL_DYNAMIC_STORAGE_BIT;
mObjHead = 0;
mObjSize = 3 * objCount * sizeof(Matrix);
glBindBuffer(GL_SHADER_STORAGE_BUFFER, mObjBuffer);
glBufferStorage(GL_SHADER_STORAGE_BUFFER, mObjSize, 0, createFlags);
mObjPtr = glMapBufferRange(GL_SHADER_STORAGE_BUFFER, 0, mObjSize, mapFlags);

## Slide 108: Cmd Buffer Update
mCmdLock.WaitForLockedRange(mCmdHead, sizeof(DEICmd) * objCount);
for (size_t u = 0; u < objCount; ++u) {
DEICmd *cmd = (mCmdPtr + mCmdHead) + u;
cmd->count = mIndexCount;
cmd->instanceCount = 1;
cmd->firstIndex = 0;
cmd->baseVertex = 0;
cmd->baseInstance = 0;
}
oldCmdHead = mCmdHead;
mCmdHead = (mCmdHead + sizeof(DEICmd) * objCount) % mCmdSize;
// Next, update the per-Object Data

## Slide 109: Fencing for fun and profit
mCmdLock.WaitForLockedRange(mCmdHead, sizeof(DEICmd) * objCount);
for (size_t u = 0; u < objCount; ++u) {
DEICmd *cmd = (mCmdPtr + mCmdHead) + u;
cmd->count = mIndexCount;
cmd->instanceCount = 1;
cmd->firstIndex = 0;
cmd->baseVertex = 0;
cmd->baseInstance = 0;
}
oldCmdHead = mCmdHead;
mCmdHead = (mCmdHead + sizeof(DEICmd) * objCount) % mCmdSize;
// Next, update the per-Object Data

## Slide 110: Someone Set Up Us The Draws
mCmdLock.WaitForLockedRange(mCmdHead, sizeof(DEICmd) * objCount);
for (size_t u = 0; u < objCount; ++u) {
DEICmd *cmd = (mCmdPtr + mCmdHead) + u;
cmd->count = mIndexCount;
cmd->instanceCount = 1;
cmd->firstIndex = 0;
cmd->baseVertex = 0;
cmd->baseInstance = 0;
}
oldCmdHead = mCmdHead;
mCmdHead = (mCmdHead + sizeof(DEICmd) * objCount) % mCmdSize;
// Next, update the per-Object Data

## Slide 111: Manage the Head
mCmdLock.WaitForLockedRange(mCmdHead, sizeof(DEICmd) * objCount);
for (size_t u = 0; u < objCount; ++u) {
DEICmd *cmd = (mCmdPtr + mCmdHead) + u;
cmd->count = mIndexCount;
cmd->instanceCount = 1;
cmd->firstIndex = 0;
cmd->baseVertex = 0;
cmd->baseInstance = 0;
}
oldCmdHead = mCmdHead;
mCmdHead = (mCmdHead + sizeof(DEICmd) * objCount) % mCmdSize;
// Next, update the per-Object Data

## Slide 112: Obj Buffer Update
// Next, update the per-Object Data
// Next, update the per-Object Data

## Slide 113: Obj Buffer Update / Render
// Next, update the per-Object Data
mObjLock.WaitForLockedRange(mObjHead, sizeof(Matrix) * objCount);
for (size_t u = 0; u < objCount; ++u) {
Matrix *obj = (mObjPtr + mObjHead) + u;
(*obj) = (inObjParameters)[u];
}
glMultiDrawElementsIndirect(GL_TRIANGLES, GL_UNSIGNED_SHORT, 0, objCount, 0);
mCmdLock.LockRange(oldCmdHead, sizeof(DEICmd) * objCount);
mObjLock.LockRange(mObjHead, sizeof(Matrix) * objCount);
mObjHead = (mObjHead + sizeof(Matrix) * objCount) % mObjSize;

## Slide 114: Seriously though, be safe
// Next, update the per-Object Data
mObjLock.WaitForLockedRange(mObjHead, sizeof(Matrix) * objCount);
for (size_t u = 0; u < objCount; ++u) {
Matrix *obj = (mObjPtr + mObjHead) + u;
(*obj) = (inObjParameters)[u];
}
glMultiDrawElementsIndirect(GL_TRIANGLES, GL_UNSIGNED_SHORT, 0, objCount, 0);
mCmdLock.LockRange(oldCmdHead, sizeof(DEICmd) * objCount);
mObjLock.LockRange(mObjHead, sizeof(Matrix) * objCount);
mObjHead = (mObjHead + sizeof(Matrix) * objCount) % mObjSize;

## Slide 115: Updates to object parameters
// Next, update the per-Object Data
mObjLock.WaitForLockedRange(mObjHead, sizeof(Matrix) * objCount);
for (size_t u = 0; u < objCount; ++u) {
Matrix *obj = (mObjPtr + mObjHead) + u;
(*obj) = (inObjParameters)[u];
}
glMultiDrawElementsIndirect(GL_TRIANGLES, GL_UNSIGNED_SHORT, 0, objCount, 0);
mCmdLock.LockRange(oldCmdHead, sizeof(DEICmd) * objCount);
mObjLock.LockRange(mObjHead, sizeof(Matrix) * objCount);
mObjHead = (mObjHead + sizeof(Matrix) * objCount) % mObjSize;

## Slide 116: Draw all the things
// Next, update the per-Object Data
mObjLock.WaitForLockedRange(mObjHead, sizeof(Matrix) * objCount);
for (size_t u = 0; u < objCount; ++u) {
Matrix *obj = (mObjPtr + mObjHead) + u;
(*obj) = (inObjParameters)[u];
}
glMultiDrawElementsIndirect(GL_TRIANGLES, GL_UNSIGNED_SHORT, 0, objCount, 0);
mCmdLock.LockRange(oldCmdHead, sizeof(DEICmd) * objCount);
mObjLock.LockRange(mObjHead, sizeof(Matrix) * objCount);
mObjHead = (mObjHead + sizeof(Matrix) * objCount) % mObjSize;

## Slide 117: Head management
// Next, update the per-Object Data
mObjLock.WaitForLockedRange(mObjHead, sizeof(Matrix) * objCount);
for (size_t u = 0; u < objCount; ++u) {
Matrix *obj = (mObjPtr + mObjHead) + u;
(*obj) = (inObjParameters)[u];
}
glMultiDrawElementsIndirect(GL_TRIANGLES, GL_UNSIGNED_SHORT, 0, objCount, 0);
mCmdLock.LockRange(oldCmdHead, sizeof(DEICmd) * objCount);
mObjLock.LockRange(mObjHead, sizeof(Matrix) * objCount);
mObjHead = (mObjHead + sizeof(Matrix) * objCount) % mObjSize;

## Slide 118: TexturedQuads
Demo!
10,000 quads using different textures
Texture is changed between every object

## Slide 120
Chart: TexturedQuads – Normalized Obj/s
| GLSBTAMultiDraw-NoSDP | GLTextureArrayMultiDraw-NoSDP | GLBindlessMultiDraw | GLSBTAMultiDraw-SDP | GLTextureArrayMultiDraw-SDP | GLNoTex | GLTextureArray | GLNoTexUniform | GLTextureArrayUniform | GLSBTA | GLBindless | GLNaive | GLNaiveUniform | D3D11Naive
 | 18.5269 | 18.5097 | 9.5505 | 9.364 | 9.3282 | 5.8164 | 5.7513 | 4.2283 | 4.1881 | 4.1325 | 2.6512 | 1.2018 | 1.012 | 1

## Slide 121
Chart: TexturedQuads – Normalized Obj/s
| GLSBTAMultiDraw-NoSDP | GLTextureArrayMultiDraw-NoSDP | GLBindlessMultiDraw | GLSBTAMultiDraw-SDP | GLTextureArrayMultiDraw-SDP | GLNoTex | GLTextureArray | GLNoTexUniform | GLTextureArrayUniform | GLSBTA | GLBindless | GLNaive | GLNaiveUniform | D3D11Naive
 | 18.5269 | 18.5097 | 9.5505 | 9.364 | 9.3282 | 5.8164 | 5.7513 | 4.2283 | 4.1881 | 4.1325 | 2.6512 | 1.2018 | 1.012 | 1

## Slide 122
Chart: TexturedQuads – Normalized Obj/s
| GLSBTAMultiDraw-NoSDP | GLTextureArrayMultiDraw-NoSDP | GLBindlessMultiDraw | GLSBTAMultiDraw-SDP | GLTextureArrayMultiDraw-SDP | GLNoTex | GLTextureArray | GLNoTexUniform | GLTextureArrayUniform | GLSBTA | GLBindless | GLNaive | GLNaiveUniform | D3D11Naive
 | 18.5269 | 18.5097 | 9.5505 | 9.364 | 9.3282 | 5.8164 | 5.7513 | 4.2283 | 4.1881 | 4.1325 | 2.6512 | 1.2018 | 1.012 | 1

## Slide 123: TexturedQuads notes
SBTA was covered at Steam Dev Days
Non-Sparse, Non-Bindless TextureArray is the fallback
Should use BufferStorage improvements
SBTA = Sparse Bindless Texture Array
Notes: BufferStorage improvements are probably worth another ~15%, bringing the total speedup to ~22x over D3D11.

## Slide 124: GLTextureArrayMultiDraw-(ε|No)SDP
Instead of loose textures, use arrays of Texture Arrays
Container contains <=2048 same-shape textures
  Shape is height, width, mipmapcount, format
Use MDI for kickoffs
Address is passed as {int; float} pair

## Slide 125
struct Tex2DAddress {
uint Container;
float Page;
};
layout (std140, binding=1) readonly buffer CB1 {
Tex2DAddress texAddress[];
};
uniform sampler2DArray TexContainer[16];
// Elsewhere (in a func, whatever)
int drawID = int(In.iDrawID);
Tex2DAddress addr = texAddress[drawID];
vec3 texCoord = vec3(In.v2TexCoord.xy, addr.Page);
vec4 texel = texture(TexContainer[addr.Container], texCoord);

## Slide 126
struct Tex2DAddress {
uint Container;
float Page;
};
layout (std140, binding=1) readonly buffer CB1 {
Tex2DAddress texAddress[];
};
uniform sampler2DArray TexContainer[16];
// Elsewhere (in a func, whatever)
int drawID = int(In.iDrawID);
Tex2DAddress addr = texAddress[drawID];
vec3 texCoord = vec3(In.v2TexCoord.xy, addr.Page);
vec4 texel = texture(TexContainer[addr.Container], texCoord);

## Slide 127
struct Tex2DAddress {
uint Container;
float Page;
};
layout (std140, binding=1) readonly buffer CB1 {
Tex2DAddress texAddress[];
};
uniform sampler2DArray TexContainer[16];
// Elsewhere (in a func, whatever)
int drawID = int(In.iDrawID);
Tex2DAddress addr = texAddress[drawID];
vec3 texCoord = vec3(In.v2TexCoord.xy, addr.Page);
vec4 texel = texture(TexContainer[addr.Container], texCoord);

## Slide 128
struct Tex2DAddress {
uint Container;
float Page;
};
layout (std140, binding=1) readonly buffer CB1 {
Tex2DAddress texAddress[];
};
uniform sampler2DArray TexContainer[16];
// Elsewhere (in a func, whatever)
int drawID = int(In.iDrawID);
Tex2DAddress addr = texAddress[drawID];
vec3 texCoord = vec3(In.v2TexCoord.xy, addr.Page);
vec4 texel = texture(TexContainer[addr.Container], texCoord);

## Slide 129
struct Tex2DAddress {
uint Container;
float Page;
};
layout (std140, binding=1) readonly buffer CB1 {
Tex2DAddress texAddress[];
};
uniform sampler2DArray TexContainer[16];
// Elsewhere (in a func, whatever)
int drawID = int(In.iDrawID);
Tex2DAddress addr = texAddress[drawID];
vec3 texCoord = vec3(In.v2TexCoord.xy, addr.Page);
vec4 texel = texture(TexContainer[addr.Container], texCoord);

## Slide 130: Questions?
graham dot sellers at amd dot com @GrahamSellers
tim dot foley at intel dot com @TangentVector
cass at nvidia dot com @casseveritt
jmcdonald at nvidia dot com @basisspace